## Slide 1: Common Grid Service Terms Motivation for NAESB Standards Request R22001 NAESB RMQ-BPS Meeting Presentation 11 April 2023
Rich Brown, Principal Investigator
Lawrence Berkeley National Laboratory
Steve Widergren, co-PI
Pacific Northwest National Laboratory
DOE Grid Modernization Laboratory Consortium (GMLC)
Grid Modern-
ization
Reliable
Secure
Affordable
Flexible
Sustain-
able
Resilient

## Slide 2: Topics
Level setting
  DOE and National Lab interest in grid services
  Standards request R22001 – objectives
  Service/performance-oriented principles
State of transmission grid services
Outcome of the WEQ-BPS R22001 work
  Service descriptions
  Examples mapping existing industry services to common services
State of retail market grid services
Desired outcome of effort

## Slide 3: DOE & National Lab Grid Service Interest
Trends: operating the electric grid is growing in complexity
  Variable renewable resource growth challenges the traditional operating paradigm
  Electrification of more end-use applications increasing demand
  Affordable communications and intelligence appearing at distribution level (infrastructure and customers)
  Greater opportunities for flexible grid-edge resources to coordinate their operation with the system
    Flexible grid-edge resources: responsive generation, storage, and demand
Challenge: integration and interoperation of vast numbers of devices, systems, and participants
  Significant equipment purchased, operated, and maintained by non-grid entities
  Technology is changing and mixture is constantly evolving
  Many technology suppliers with various novel solutions
  Many jurisdictions with different rules, regulations, and business processes
National labs (GMLC) working on standard Energy Services Interface (ESI) to improve interoperability of grid-edge resources
  Builds on a foundation of common grid service definitions

## Slide 4: Standards Request R22001
Objective:
  Classify common grid services that accommodate the diverse grid needs in different regions
  Define common grid service types for wholesale power system interactions
  Derive commonalities and important variations found in existing grid services
  Meet near to mid-future needs gathered from major US ISO/RTOs and utilities
  Accommodate specialization: performance characteristics and expectations
    Qualification, performance expectations, monitoring, reconciliation, and settlement vary by operational policy of each region
    But defining common policy was beyond the scope of the effort
Benefit:
  Provides consistent service-type names, definitions, and performance characteristics
  Encourages adoption of consistent terminology in wholesale markets
  Provides starting place for retail-level grid service interactions with flexible, grid-edge resources

## Slide 5: Service-Oriented Principles
Important to distinguish grid Operational Objectives from Services
Operational objectives describe why a service is used
  Use cases help describe the desired performance characteristics from a service
  Examples: schedule energy to meet peak load forecast, or reserve energy for outage contingency
Services define what is to be performed – not how
  Example: generation needs to be at nominal power level 100 MW in 10 minutes and maintained for 1 hour
  Any equipment type that meets the performance requirement can provide the service
Service provider understands what to do, where, and when – not why
  Boundaries of responsibility are clearly understood between service requester and provider
  The service requestor’s reasons for invoking the service (the operational objectives) are hidden
  Example: a gas-turbine generator does not need to know it is scheduled for peak-load coverage
Benefits
  Decouples areas of concern – makes integration simpler, cleaner, modular
  Same service can be used to address multiple objectives
  Accommodates service provider technology decisions within performance requirements

## Slide 6: State of Grid Services – GMLC Review
Literature review
Summary of transmission grid service categorization models
  Denholm, Cappers, FERC, NERC, PNNL’s grid services report, etc.
Performance expectations v. operational objectives
Review and correlation of transmission grid service terms and definitions
  FERC, NERC, CAISO, PJM, SPP, Hawaiian Electric
State of Common Grid Services Definitions, GMLC report:
https://escholarship.org/uc/item/75d2n2dw

## Slide 7: Outcome of WEQ R22001 Effort
Classification of a (small) set of grid services
Common names for these grid-service types
Clear definitions of the service types
  Parameterized performance expectations (i.e., electrical attributes, timing attributes)
  Accommodate necessary specialization
Effort did NOT,
  Propose a uniform market policy on services
  Prescribe a solution for DER integration into wholesale electric markets
  Specify DER management technology or platforms

## Slide 8: Summary of Common Grid Services

## Slide 9: Format of Work Product
Grid service name: short title of the service
Description: short (1- or 2-sentence) definition of the service
Performance expectation: parameters that describe the expected performance delivered
  Electrical attributes:
    Electricity-related quantities or qualities (e.g., power, energy, voltage level) over the performance period.
    Electrical location: the physical location where the service is delivered in the electric system.
  Timing attributes:
    Delivery schedule: period over which the grid service is expected to take place.
    Delivery schedule notification: timing associated with notification that the delivery schedule for a service is established.
    Response time: Response time is the allowed elapsed time between the moment when the grid service is to start and the moment when the desired behavior meets the defined threshold for a given grid service.
Performance determination: typical ways the service is measured for verification
Additional information missing from standard
  Example service requestor operational objectives: applications for calling the service
  Origin of service definition: context or background on why the service exists

## Slide 10: Grid Services – WEQ-000 definitions
Energy Grid Service: A type of service in which a resource provides a quantity of energy over a scheduled period of operation.
Reserve Grid Service: A type of service in which a resource provides energy when called upon by the system operator over a commitment period.
Regulation Grid Service: A type of service in which a resource continuously increases and decreases energy in response to real-time signals from the system operator over a commitment period.
Frequency Response Grid Service: A type of service in which a resource reacts or responds to a change in system frequency by altering its power levels
Voltage Management Grid Service: A type of service in which a resource provides voltage support within a specified upper and lower voltage range over a commitment period.
Blackstart Grid Service: A type of service in which a resource can energize or remain energized without an outside electrical supply.

## Slide 11: Attribute Summary
Grid Service | Energy | Reserve | Regulation | Frequency Response | Voltage Mgmt | Blackstart
Electrical Attributes | energy (quantity) | energy (quantity) | power (level) | percent droop | target voltage or range | power (level)
 | power (level) | power (level) | power regulation range | deadband | electrical location | power regulation range
 | electrical location | electrical location | power mileage | electrical location |  | electrical location
 |  |  | electrical location |  |  | 
Timing Attributes | delivery schedule | delivery schedule | delivery schedule | delivery schedule | delivery schedule | delivery schedule
 | del sched notification | del sched notification | del sched notification | del sched notification | del sched notification | del sched notification
 |  | speed of response | speed of response |  | signal periodicity | speed of response
 |  |  | signal periodicity |  |  | 
Performance Determinations | agreements specify: a) measurement equipment and location, b) measurement units and frequency, and c) calculations of estimating methods. Examples: revenue grade energy interval meters or periodic power measurements to estimate energy. | agreements specify how performance is quantified such as energy interval meters and time-stamped power measurements. | agreements specify how real power increase or decrease is measured. A performance score or index mechanism may be applied. | agreements specify how performance is quantified with frequency response measurements. | agreements specify how performance is quantified. | agreements specify how performance is quantified.

## Slide 12: Industry Energy Grid Service Examples
 |  | CAISO - DA & Hourly | SPP - DA & RT Balancing | PJM - DA & RT
Grid Service | Energy | Energy Services | Energy Service | Energy Market
Electrical Attributes | energy (quantity) | MWh | MWh | MWh
 | power (level) | MW, $/MW curve | MW, $/MW curve | MW, $/MW curve
 | electrical location | producing & delivery nodes | ENodes linked to PNodes | pnode tied to physical connect
Timing Attributes | delivery schedule | DA 24 hrs, Hour: 1 hr prior in 5-min increments | DA 24 hrs, RTBM: 30 min prior in 5-min increments | DA 24 hrs, RT: 65 min prior in 5-min increments
 | del sched notification | DA 1pm day prior, Hour: 45-min prior | DA 1pm day prior, RTBM: not published prior | DA 1:30pm w/ rebidding 2:15pm day prior, RT: not published prior
Performance Determinations | agreements specify: a) measurement equipment and location, b) measurement units and frequency, and c) calculations of estimating methods. Examples: revenue grade energy interval meters or periodic power measurements to estimate energy. | revenue quality energy interval meter certified by CAISO reading at point of interconnection. 5- or 15-minute intervals. Estimation procedure used if there is a measurement failure. | revenue quality energy meters at the Pnodes at least hourly or every 5 minutes synchronized to delivery intervals. Real-time power used as backup | “For each hour of the Operating Day, PJM calculates an hourly-integrated telemetry MWh value using the time-weighted telemetry MW values for each of the five-minute intervals in the hour”

## Slide 13: Industry Reserve Grid Service Examples
 |  | CAISO - DA & Hourly |  | SPP - DA & RT | 
Grid Service | Reserve | Spinning | Non-spinning | Spinning | Supplemental
Electrical Attributes | energy (quantity) |  |  | MWh | MWh
 | power (level) | MW, $/MW curve | MW, $/MW curve | MW, $/MW curve | MW, $/MW curve
 | electrical location | ancillary service region | ancillary service region | reserve zone | reserve zone
Timing Attributes | delivery schedule | DA 24 hrs, Hour: 1 hr prior | DA 24 hrs, Hour: 1 hr prior | DA 24hrs, RT 30-min prior | DA 24hrs, RT 30-min prior
 | del sched notification | DA 1pm day prior, Hour: 45-min prior | DA 1pm day prior, Hour: 45-min prior | DA 6am day prior, Hour: not published prior | DA 1pm day prior, Hour: not published prior
 | speed of response | 1 min | 10 min | 10 min from online | 10 min from offline
Performance Determinations | agreements specify how performance is quantified such as energy interval metersand time-stamped power measurements. | Selected equipment is to be on-line | settlement quality energy meter in 5-min intervals | equipment capable to respond within 10 min of notice | revenue quality energy meter in 5 min intervals. Where unavailable telemetered power scanned every 10 sec.

## Slide 14: State of Retail grid-DER Services
Drivers for coordinating DER flexible operation has largely been wholesale market driven
Retail engagement terms have been program-oriented, not service-oriented
  Demand response
  Demand-side management
  Demand caps
  Congestion management
  Emergency load reduction
  Time-variable pricing programs
    Time-of-use
    Dynamic time-of-use
    Peak pricing
    Critical peak pricing
    Real-time pricing
    Day-ahead pricing
Observations
Programs named and designed around operational objectives rather than the service to be provided.
The services seem to fall into a couple categories:
          A. energy grid-DER service
          B. reserve grid-DER service
          Other wholesale grid services not yet practical

## Slide 15: Desired Outcome of Effort
Classification of a (small) set of grid services for retail markets
  Consistent with R22001 if possible
Common names for these grid-service types
Clear definitions of the service types
  Parameterized performance expectations (i.e., electrical attributes, timing attributes)
  Accommodate necessary specialization
Examples of how existing retail grid-DER programs map into common services
As much commonality as possible between wholesale and retail grid services
Effort does NOT,
  Propose a uniform market policy on retail services
  Prescribe a single solution for DER integration into wholesale or retail electric markets
  Specify DER management technology or platforms